PacketFence
– version 1.9.1
Installation Guide

Copyright © 2008-2010 Inverse inc. (http://inverse.ca)
Permission is granted to copy, distribute and/or modify this document under the terms of the GNU Free Documentation License, Version 1.2 or any later version published by the Free Software Foundation; with no Invariant Sections, no Front-Cover Texts, and no Back-Cover Texts. A copy of the license is included in the section entitled “GNU Free Documentation License”.
Version 1.9.1 – September 2010
Contents

# About this Guide
This guide will walk you through the installation and configuration of the PacketFence solution. It covers VLAN isolation setup.
The instructions are based on version 1.9.1 of PacketFence.
The latest version of this guide is available online at
http://www.packetfence.org/download/documentation.html
# System Requirements
## Assumptions
PacketFence reuses many components in an infrastructure. Thus, it requires the following ones:
❏	Database server (MySQL)
❏	Web server (Apache)
Depending on your setup you may have to install additional components like:
❏	DHCP server (ISC DHCP)
❏	DNS server (BIND)
❏	NIDS (Snort)

In this guide, we assume that all those components are running on the same server (i.e., “localhost” or “127.0.0.1”) that PacketFence will be installed on.
Good understanding of those underlying component and GNU/Linux is required to install PacketFence. If you miss some of those required components, please refer to the appropriate documentation and proceed with the installation and configuration of these requirements before continuing with this guide.
The following table provides recommendations for the required components, together with version numbers :
MySQL server	MySQL 4.1 or 5.1
Web server	Apache 2
ISC DHCP	DHCP 3
ISC BIND	BIND 9
Snort	Snort 2.8

More recent versions of the software mentioned above can also be used.
## Minimum Hardware Requirements
The following table provides hardware recommendations for the server and desktops :
Server	◾ Intel or AMD CPU 3 GHz / ◾ 2048 MB of RAM / ◾ 20 GB of disk space (RAID 1) / ◾ 3 Network cards

## Operating System Requirements
PacketFence 1.9.1 supports the following operating systems on the i386 or x86_64 architectures:
❏	Red Hat Enterprise Linux 5.x Server
With the EPEL (Extra Packages for Enterprise Linux) repository enabled. It is disabled by default. Here are instructions to enable that repository: http://fedoraproject.org/wiki/EPEL/FAQ#howtouse
❏	Community ENTerprise Operating System (CentOS) 5.x
With the extras yum repository enabled. It is enabled by default.

Make sure the required components are started automatically (except Snort and Apache that are controlled by PacketFence) at boot time and that they are running before proceeding with the PacketFence configuration. Also make sure that you can install additional packages from your standard distribution. For example, if you are using Red Hat Enterprise Linux 5, you have to be subscribed to the Red Hat Network before continuing with the PacketFence software installation.
Other distributions such as Debian, Fedora and Gentoo are known to work but this document won't cover them.
# Installation
This section will guide you through the installation of PacketFence together with its dependencies.
## OS Installation
Install CentOS 5 or RedHat Enterprise Linux 5 with minimal installation and no additional packages. Then:
❏	Enable Firewall
❏	Disable SELinux
Make sure your system is up to date and your yum database is updated:
yum update
Some PacketFence dependencies are available through the DAG repository (http://dag.wieers.com/) so you need to configure YUM to use it.
First import the DAG RPM GPG key:
rpm -import http://dag.wieers.com/rpm/packages/RPM-GPG-KEY.dag.txt
Then install the latest version of the RPMForge package (http://dag.wieers.com/rpm/packages/rpmforge-release/):
rpm -i rpmforge-release-0.3.6-1.el5.rf.i386.rpm

## Software Download
Starting with 1.8.5, PacketFence is now provided as an RPM repository for Red Hat Enterprise Linux 5 / CentOS 5 instead of a single RPM file.
This repository contains all required dependencies to install PacketFence. This provides numerous advantages:
❏	very easy installation
❏	everything is packaged as RPM (no more CPAN hassle)
❏	easy upgrade
## Software Installation
In order to use the repository, just create a file named /etc/yum.repos.d/PacketFence.repo with the following content:
[PacketFence]
name=PacketFence Repository baseurl=http://inverse.ca/downloads/PacketFence/RHEL5/$basearch
gpgcheck=0
Once the repository is defined, you can install PacketFence with all it's dependencies, and the required external services (BIND/MySQL/DHCP/FreeRadius2) using:
yum groupinstall “Packetfence-Complete”
If you prefer to install only the core PacketFence without all the external services, you can use :
yum install packetfence
Execute the installer at /usr/local/pf/installer.pl and follow the instructions.
Once completed, PacketFence will be fully installed on your server. You are now ready to configure it.
# Configuration
In this section, you'll learn how to configure PacketFence with VLAN isolation. PacketFence will use MySQL, Apache, ISC DHCP, ISC DNS. As previously mentioned, we assume that those components run on the same server on which PacketFence is being installed.
## General Configuration
Set the timezone in /etc/php.ini. For example:
date.timezone="America/Montreal”

Execute the configurator at /usr/local/pf/configurator.pl to configure PacketFence according your needs.
## Apache Configuration
The PacketFence configuration for Apache is located in /usr/local/pf/conf/templates/httpd.conf.
Upon PacketFence installation, a default configuration file is created which is suitable for most configurations. SSL is enabled by default to secure access.
Remember that SELinux must be disabled.

## Authentication (flat file, LDAP, Radius)
PacketFence can authenticate users that register devices using a flat file, an LDAP server or a Radius server.
Flat file
By default, PacketFence looks into /usr/local/pf/conf/user.conf to find users allowed to register devices. If you want to use a different file, edit /usr/local/pf/conf/authentication/local.pm and change the following parameter :
my $passwdFile = '/usr/local/pf/conf/user.conf';
You need to encrypt the password of each user with htpasswd like this :
htpasswd /usr/local/pf/conf/user.conf newuser
Enter the password twice

LDAP
Edit /usr/local/pf/conf/authentication/ldap.pm and make the necessary changes to the following parameters :
my $LDAPUserBase = "ou=People,dc=domain,dc=edu";
my $LDAPUserKey = "uid";
my $LDAPUserScope = "one";
my $LDAPBindDN = "cn=ldapuser,dc=domain,dc=edu";
my $LDAPBindPassword = "password";
my $LDAPServer = "127.0.0.1";

Radius
Edit /usr/local/pf/conf/authentication/radius.pm and make the necessary changes to the following parameters :
my $RadiusServer = 'localhost';
my $RadiusSecret = 'testing123';

Selecting an Authentication Method
To configure authentication set the [registration].auth option in /usr/local/pf/conf/pf.conf:
auth=local,ldap,radius
If more than one method are specified, PF will display a pull-down list to allow users to select the preferred authentication method.

## VLAN isolation
Assumptions
Throughout this configuration example we use the following assumptions for our network infrastructure:
❏	There are two different types of manageable switches in our network: Cisco Catalyst 2900XL and Cisco Catalyst 2960
❏	VLAN 1 is the “regular” VLAN
❏	VLAN 2 is the registration VLAN (unregistered devices will be put in this VLAN)
❏	VLAN 3 is the isolation VLAN (isolated devices will be put in this VLAN)
❏	VLAN 4 is the MAC detection VLAN (empty VLAN)
❏	VLANs 2 and 3 are spanned throughout the network
❏	VLAN 4 must be defined on all the switches that do not support port-security (in our example Catalyst 2900XL do not support port-security with static MAC address). No need to put it in the trunk port.
❏	We want to isolate computers using Limewire
❏	We use Snort as NIDS. Refer to Snort web site for installation and configuration instructions
❏	Since Snort sees only the IP address of the devices and PacketFence's database is indexed by MAC, we span the DHCP traffic to PacketFence so it always knows the IP-MAC association. We use eth1 on PacketFence for the DHCP span (Refer to your switch configuration for SPAN setup)
❏	The traffic monitored by Snort is spanned on eth2
❏	The DHCP server on the PacketFence box that will take care of IP address distribution in VLANs 2 and 3
❏	The DNS server on the PacketFence box that will take care of domain resolution in VLANs 2 and 3

❏	The network setup looks like this:
VLAN ID	VLAN Name	Subnet	Gateway	PacketFence Address
1	Normal	192.168.1.0/24	192.168.1.1	192.168.1.5
2	Registration	192.168.2.0/24	192.168.2.1	192.168.2.1
3	Isolation	192.168.3.0/24	192.168.3.1	192.168.3.1
4	Mac Detection
100	Voice

Network Interfaces
Here are the NICs startup scripts on PacketFence:
❏	/etc/sysconfig/network-scripts/ifcfg-eth0
DEVICE=eth0
BROADCAST=192.168.1.255
IPADDR=192.168.1.5
NETMASK=255.255.255.0
NETWORK=192.168.1.0
ONBOOT=yes
TYPE=Ethernet
❏	/etc/sysconfig/network-scripts/ifcfg-eth0.2
DEVICE=eth0.2
ONBOOT=yes
BOOTPROTO=static
IPADDR=192.168.2.1
NETMASK=255.255.255.0
VLAN=yes
❏	/etc/sysconfig/network-scripts/ifcfg-eth0.3
DEVICE=eth0.3
ONBOOT=yes
BOOTPROTO=static
IPADDR=192.168.3.1
NETMASK=255.255.255.0
VLAN=yes

❏	/etc/sysconfig/network-scripts/ifcfg-eth1. This NIC is used for the span of DHCP traffic.
DEVICE=eth1
ONBOOT=yes
BOOTPROTO=none
❏	/etc/sysconfig/network-scripts/ifcfg-eth2. This NIC is used for the span of traffic monitored by Snort.
DEVICE=eth2
ONBOOT=yes
BOOTPROTO=none

Trap receiver
PacketFence uses snmptrapd as the trap receiver. It stores the community name used by the switch to send traps in the switch config file (/usr/local/pf/conf/switches.conf):
[default]
SNMPCommunityTrap = public

Switch Setup
In our example, we enable linkUp/linkDown + MAC Notification on 2900XL and Port Security on 2960. Please consult the Administration Guide for the complete list of supported switches and configuration instructions.
❏	linkUp/linkDown + MAC Notification
global setup
snmp-server enable traps snmp linkdown linkup
snmp-server enable traps mac-notification
snmp-server host 192.168.1.5 trap version 2c public snmp mac-notification
mac-address-table notification interval 0
mac-address-table notification
mac-address-table aging-time 3600

On each interface
switchport mode access
switchport access vlan 4
snmp trap mac-notification added
There are no parameters needed on each interface for linkUp/linkDown traps since these traps are enabled globally for all the ports.

❏	Port Security
global setup
snmp-server enable traps port-security
snmp-server enable traps port-security trap-rate 1
snmp-server host 192.168.1.5 version 2c public port-security
On each interface, you need to initialize the port security by authorizing a fake MAC address with the following commands
switchport access vlan 4
switchport port-security
switchport port-security maximum 2
switchport port-security maximum 1 vlan access
switchport port-security violation restrict
switchport port-security mac-address 0200.0000.00xx
where xx stands for the interface index
Don't forget to update the startup-config

Logs
The log config file is /usr/local/pf/conf/log.conf. It contains the configuration for Log::Log4Perl and you normally don't need to modify it.

Switch Definition
PacketFence needs to know which switches it manages and their type and configuration. All this information is stored in /usr/local/pf/conf/switches.conf.
This files contains a default section including:
❏	List of VLANs managed by PacketFence
❏	Default SNMP read/write communities for the switches
❏	Default working mode (see note about working mode below)
and a switch section for each switch (managed by PacketFence) including:
❏	Switch IP
❏	Switch vendor/type (so that the correct subclasses of pf::SNMP are instantiated)
❏	Switch uplink ports (trunks and non-managed ports)
❏	per-switch re-definition of the vlans (if required)

Working modes
There are three different working modes:
❏	Testing: pfsetvlan writes in the log files what it would normally do, but it doesn't do anything.
❏	Registration: pfsetvlan automatically-register all MAC addresses seen on the switch ports. As in testing mode, no VLAN changes are done.
❏	Production: pfsetvlan sends the SNMP writes to change the VLAN on the switch ports.
CAUTION: If [trapping.testing] (see pf.conf) is enabled, PacketFence will consider that all the switches are in test whatever the working mode is !

Here are the parameters (other than the defaults ones) for our example
[default]
SNMPCommunityRead = public
SNMPCommunityWrite = private
SNMPommunityTrap = public
SNMPVersion = 1
vlans = 1,2,3,4,10
normalVlan = 1
registrationVlan = 2
isolationVlan = 3
macDetectionVlan = 4
VoIPEnabled = no
[192.168.1.100]
type = Cisco::Catalyst_2900XL
mode = production
uplink = 24
[192.168.1.101]
type = Cisco::Catalyst_2960
mode = production
uplink = 25
normalVlan = 10
If you want to have a different read/write communities name for each switch, declare it in each switch section
Once you have modified switches.conf for your network, you can execute some first tests (only SNMP reads) using the supplied /usr/local/pf/test/connect_and_read.pl script.
Custom Trap Handling Functions
Pfsetvlan is the daemon responsible of trap handling. When it receives a trap, pfsetvlan uses some functions defined in pf::vlan::custom in order to know what to do.
For example, custom_getCorrectVlan() allows you to define what you consider to be the correct VLAN for a given switch port and connected MAC. In our example there is only one VLAN (VLAN 1) so the function should look like
sub custom_getCorrectVlan {
 my ($switch_ip, $ifIndex, $mac, $status, $vlan, $pid) = @_;
 my $logger = Log::Log4perl->get_logger();
 Log::Log4perl::MDC->put('tid', threads->self->tid());
 return 1;
}
If all your VLANs are configured in switches.conf you might want to keep the default definition. Under this configuration, the correct default VLAN for a given MAC is the normalVlan variable of the switch where the MAC is connected or the [default] normalVlan if the switch doesn't specify a normalVlan.
If, on the other hand, you have many VLANs depending on your physical location (building, campus) or MAC attributes, you need to put some more effort into this function to redefine it.
Have look at the other functions and make sure they fit your needs.
pf.conf
The /usr/local/pf/conf/pf.conf file contains the PacketFence general configuration. For example, this is the place where we inform PacketFence it will work in VLAN isolation mode.
All the default parameters and their descriptions are stored in /usr/local/pf/conf/pf.conf.defaults.
In order to override a default parameter, define it and set it in pf.conf.
See the Administration Guide for the complete list of all available parameters.

Here is the pf.conf file for our setup:
[general]
domain=yourdomain.org
dnsservers=192.168.2.1,192.168.3.1
dhcpservers=192.168.2.1,192.168.3.1
[network]
mode=vlan
[trapping]
registration=enabled
detection=enabled
testing=disabled
range=192.168.2.0/24,192.168.3.0/24
[registration]
auth=ldap
[interface eth0]
mask=255.255.255.0
type=internal,managed
gateway=192.168.1.1
ip=192.168.1.5
[interface eth0.2]
mask=255.255.255.0
type=internal
gateway=192.168.2.1
ip=192.168.2.1
[interface eth0.3]
mask=255.255.255.0
type=internal
gateway=192.168.3.1
ip=192.168.3.1
[interface eth1]
mask=255.255.255.0
type=dhcplistener
gateway=192.168.1.5
ip=192.168.1.254
[interface eth2]
mask=255.255.255.0
type=monitor
gateway=192.168.1.5
ip=192.168.1.1

Iptables
You need to open the following ports in Iptables:
❏	53 (DNS), 80 (HTTP), 443 (HTTPS) on eth0.2 and eth0.3
❏	162 (SNMP) and 1443 (Web Admin Interface) on eth0

Here are the /etc/sysconfig/iptables lines for our setup:
-A RH-Firewall-1-INPUT -p udp -m udp --dport 53 -s 192.168.2.0/24 -d 192.168.2.1 -i eth0.2 -j ACCEPT
-A RH-Firewall-1-INPUT -p udp -m udp --dport 53 -s 192.168.3.0/24 -d 192.168.3.1 -i eth0.3 -j ACCEPT
-A RH-Firewall-1-INPUT -p tcp -m tcp --dport 80 -s 192.168.2.0/24 -d 192.168.2.1 -i eth0.2 -j ACCEPT
-A RH-Firewall-1-INPUT -p tcp -m tcp --dport 80 -s 192.168.3.0/24 -d 192.168.3.1 -i eth0.3 -j ACCEPT
-A RH-Firewall-1-INPUT -p udp -m udp --dport 162 -d 192.168.1.5 -i eth0 -j ACCEPT
-A RH-Firewall-1-INPUT -p tcp -m tcp --dport 443 -s 192.168.2.0/24 -d 192.168.2.1 -i eth0.2 -j ACCEPT
-A RH-Firewall-1-INPUT -p tcp -m tcp --dport 443 -s 192.168.3.0/24 -d 192.168.3.1 -i eth0.3 -j ACCEPT
-A RH-Firewall-1-INPUT -p tcp -m tcp --dport 1443 -d 192.168.1.5 -i eth0 -j ACCEPT

DHCP
The DHCP server will manage IP distribution in VLANs 2 and 3.
Put the following line in /etc/sysconfig/dhcpd:
DHCPDARGS="eth0.2 eth0.3"
Edit /etc/dhcpd.conf and replace its content with:
authoritative;
ddns-update-style none;
ignore client-updates;
subnet 192.168.2.0 netmask 255.255.255.0 {
 option routers 192.168.2.1;
 option subnet-mask 255.255.255.0;
 option domain-name "registration.example.com";
 option domain-name-servers 192.168.2.1;
 range 192.168.2.2 192.168.2.254;
 default-lease-time 300;
 max-lease-time 600;
}
subnet 192.168.3.0 netmask 255.255.255.0 {
 option routers 192.168.3.1;
 option subnet-mask 255.255.255.0;
 option domain-name "isolation.example.com";
 option domain-name-servers 192.168.3.1;
 range 192.168.3.2 192.168.3.254;
 default-lease-time 300;
 max-lease-time 600;
}

DNS
The DNS server will answer to all domain resolution requests in VLANs 2 and 3.

Create /etc/named.conf with the following content:
options {
 directory "/var/named";
 dump-file "/var/named/data/cache_dump.db";
 statistics-file "/var/named/data/named_stats.txt";
 listen-on { 192.168.2.1; 192.168.3.1; };
};
controls {
 inet 127.0.0.1 allow { localhost; } keys { rndckey; };
};
view "registration" {
  match-clients { 192.168.2.0/24; };
  zone "." IN {
    type master;
    file "named-registration.ca";
  };
};
view "isolation" {
  match-clients { 192.168.3.0/24; };
  zone "." IN {
    type master;
    file "named-isolation.ca";
  };
};
include "/etc/rndc.key";

Create /var/named/named-registration.ca with the following content:
$TTL 3600
. IN SOA pf. admin.example.com (
   2005061501 ; serial
   10800 ; refresh
   3600 ; retry
   604800 ; expire
   86400 ; default_ttl
)
       IN NS pf.
*. IN A 192.168.2.1
      IN MX 5 pf.
1.2.168.192.in-addr.arpa. IN PTR pf
Create /var/named/named-isolation.ca with the following content:
$TTL 3600
. IN SOA pf. admin.example.com (
   2005061501 ; serial
   10800 ; refresh
   3600 ; retry
   604800 ; expire
   86400 ; default_ttl
)
       IN NS pf.
*. IN A 192.168.3.1
      IN MX 5 pf.
1.3.168.192.in-addr.arpa. IN PTR pf

## Violations
In our example we want to isolate people using Limewire. Here we assume Snort is installed and configured to send alerts to PacketFence. Now we need to configure PacketFence isolation.
Enable Limewire violation in /usr/local/pf/conf/violations.conf and configure it to execute an external script
[2001808]
desc=P2P (Limewire)
priority=8
url=/content/index.php?template=p2p
actions=log,trap
disable=N
max_enable=1
trigger=Detect::2001808

## Starting Services
Once PacketFence is fully installed and configured, start the services using the following command :
service packetfence start
You may verify using the chkconfig command that the PacketFence service is automatically started at boot time.
# Testing
## PacketFence Web Interface
To test the PacketFence admin interface, go to the following URL : https://pf.yourdomain.org:1443.
Log in using the “admin” user and the password you defined earlier when running installer.pl.
## VLAN Isolation
There many tests that you need to do in order to make sure everything works fine.

Make sure that VLANs 2,3 and 4 are not routed anywhere and can not communicate with the rest of the network:
❏	any device in VLAN 2 can communicate with PacketFence through (and only through) eth0.2
❏	any device in VLAN 2 can not communicate with any device in any other VLAN
❏	any device in VLAN 3 can communicate with PacketFence through (and only through) eth0.3
❏	any device in VLAN 3 can not communicate with any device in any other VLAN
❏	any device in VLAN 4 can not communicate with any device in any other VLAN

Make sure PacketFence receives traps from the switches:
❏	configure the Catalyst 2900 switch to send linkUp/linkDown traps to PacketFence
❏	configure the Catalyst 2960 switch to send port-security traps to PacketFence
❏	plug a device on each switch
❏	make sure snmptrapd writes a line in /usr/local/pf/logs/snmptrapd.log
Make sure each trap is correctly decoded by pfsetvlan. Make sure there are no error messages in /usr/local/pf/logs/error* nor in /usr/local/pf/logs/packetfence.log while PacketFence starts
Plug an unregistered computer in a switch and make sure:
❏	the port is put in VLAN 2
❏	the computer gets an IP in VLAN 2
❏	any DNS request resolves to PacketFence (use nslookup (for example)
❏	the computer can access the registration web page

Register the computer by following the instructions in the registration web pages and make sure that when computer reboots it has access to VLAN 1.

Install Limewire on the test computer (Snort log its activity in /var/log/snort/*). Start using it and make sure:
❏	the computer is put in VLAN 3 (see /usr/local/pf/logs/packetfence.log)
❏	you can see a message in the browser explaining why the computer is isolated
❏	you can re-enable your network access on your own
# Additional Information
For more information, please consult the mailing archives or post your questions to it. For details, see :
packetfence-announce@lists.sourceforge.net: Public announcements (new releases, security warnings etc.) regarding PacketFence
packetfence-devel@lists.sourceforge.net: Discussion of PacketFence development
packetfence-users@lists.sourceforge.net: User and usage discussions

# Commercial Support and Contact Information
For any questions or comments, do not hesitate to contact us by writing an email to :
support@inverse.ca
Inverse (http://inverse.ca) offers professional services around PacketFence to help organizations deploy the solution, customize, migrate versions or from another system, performance tuning or aligning with best practices.
Hourly rates or support packages are offered to best suit your needs.
Please visit http://inverse.ca/support.html for details.
# GNU Free Documentation License
Please refer to http://www.gnu.org/licenses/fdl-1.2.txt for the full license.